## Slide 1: Biomass stoves in dwellings: interplays between fuel use & technology
pellet stove design challenge 2016
brookhaven, new york, usa
*Ricardo L. Carvalho1,2, Ole M. Jensen1, Luís A. Tarelho2, Estela D. Vicente2
1Department of Energy and Environment, SBi, Aalborg University, Denmark
2Department of Environment & Planning, CESAM, Aveiro University, Portugal
Notes: Bringing stories around the Europe…

## Slide 2: Biomass stoves in dwellings: interplay between fuel use and technology
Solid-fuel use & air pollution
Traditional installations & certified appliances
Comparing two contexts
Performance: retrofits & automation
Advanced interventions
Outcomes

## Slide 3
Solid-fuel use & air pollution
In cold areas, heating requires more fuel than cooking during atmospheric inversions!
Residential wood heating is a major source of PM in Europe
Notes: Outdoor air pollution is a major risk factor – responsible for 3.3 million permature deaths from PM2.5 associated to residential energy use in India and China (GBD, 2010)

## Slide 4
Traditional installations & certified appliances
Heating and cooking using wood/coal in Spain, Galician cast-iron stove, 2013
Recreational wood heat in Europe
Open fire, 2016
© Carvalho,2013
Notes: Direct wood heaters dominate LOT15 stock ~ 65 Mo
e.g. Fireplaces (16 Mo)
e.g. Enclosed (>7 Mo)

## Slide 5
Traditional (22 Mo) & certified appliances (41 Mo)
Heating and cooking in Spain,
Galician cast-iron stove, 2013
Recreational wood heat in Europe
Open fire, 2014
All over Europe
Wide range loads
1-6 kg/h
Rural Areas
Mediterranean
High loads
2-4 kg/h
© Carvalho,2013
Primary Mediterranean High loads
Secondary Nordic
Low loads
Heating winter in Spain. Portugal
Insert, 2016
Heating and cosiness , winter in Denmark, 2014
EN ecolabel Portugal
© Solzaima,2016
Ecolabel swan
Notes: e.g. Certified inserts >16 Mo
e.g. Certified roomheaters >25 Mo

## Slide 6: Comparing two contexts
Portugal
~1.5 Mo installations
Chart: 
| Fireplace | Old closed | New closed | Modern | Boilers and cookers

35.342 TJ/primary heat
11 kt PM2.5
Denmark
~0.7 Mo installations
31.190 TJ/secondary heat
~30% pellet boilers/stoves!
17 kt PM2.5
Chart: 
| Fireplace | Old closed (pre-1990) | New closed (1990-2005) | Modern (post 2005) | Boilers and cookers
 | 645818.0545 | 282902.5991 | 294333.0071 | 0 | 272900.992

Chart: 
| Fireplace | Old closed (pre-1990) | New closed (1990-2005) | Modern (post 2005) | Boilers and cookers
 | 16210 | 157500 | 292500 | 300000 | 46638

C. Gonçalves et al. Inventory of fine particulate organic compound emissions from residential wood combustion in Portugal. Atmospheric Environment, 50, 297-306, 2012.
Danish Centre for Energy and Environment, 2013.

## Slide 7: Performance: retrofits & automation Simulating real-world emissions
(3) Dilut. tunnel in a testing setting (NS3058)
Denmark, 2010
Natural draft
Ecodesign requirements,
ANNEX III; 4.a (2)
Ecodesign requirements,
ANNEX III; 4.a (3)
12Pa
© Carvalho,2014
(2) Dilution tunnel at Univ. of Aveiro
Dilution rate/25-35
Portugal, 2015

## Slide 8
Flow meter
Kurz 155
FTIR
Gasmet
CX4000
Iberic rural house
Pellet stove (EN14785:2008), 2016
Pitot
Testo 512
TCR/Tecora
6ms-1/2.3 m3/h
© Tarelho, 2015
Gaseous (mg/Nm3) 13% O2
Particulate (g/kgF) emissions
Thermal efficiency (%)
Wattage output (kW)
Laboratory tests
3 installations
Performance: retrofits & automation Laboratory & field studies
Notes: Ftir = fourier transform infrared analyzer
1- Moisture/Ash (CE N14774/5;EN14961-2)
2-Elemental analysis
(external lab)

## Slide 9: Performance: retrofits Operation of wood stove (B) & heat recovery
Stove B
B+Chimney pre-heating

## Slide 10: Performance: retrofits & automation Gaseous (CO and TOCs) emissions (N=3)
Chart: CO emissions (mg/Nm3)
| Fireplace A (1.6 kg/h) | Wood stove B (2.6 kg/h) | B+Secondary air (2.4 kg/h) | B+Pre-heated air (1.4 kg/h) | Pellet stove C (1.1 kg/h;EN-plus) | Pellet stove C (1.7 kg/h;local)
CO 13%O2 (mg/Nm3) | 4601.3292 | 5830.9161 | 4462.3011 | 4622.2112 | 897.6971 | 142.554
TOC 13%O2 (mgC/Nm3) | 427.5272 | 320.3195 | 270.4583 | 238.8981 | 13.3031 | 2.6222
Ecodesign (mg/Nm3) | 2000 | 120 | 500 | 120 | 500 | 120 | 500 | 120 | 300 | 60 | 300 | 60
The European Comission, “Implementing Directive 2009/125/EC of the European Parliament and of the Council with regard to ecodesign requirements for solid fuel local space heaters,” Off. J. Eur. Union, pp. 1–19, 2015. ANNEX II

## Slide 11: Performance: automation Thermal efficiency and PM emissions (N=3)
E. D. Vicente, M. A. Duarte, L. A. C. Tarelho et al, “Particulate and gaseous emissions from the combustion of different biofuels in a pellet stove,” Atmos. Environ., vol. 120, pp. 15–27, 2015.
Chart: Thermal efficiency (η)
| Fireplace A (1.6 kg/h) | Wood stove B (2.6 kg/h) | B+Secondary air (2.4 kg/h) | B+Pre-heated air (1.4 kg/h) | Pellet stove C (1.1 kg/h;EN-plus) | Pellet stove C (1.7 kg/h;local)
η (%) | 29.9084 | 64.7462 | 56.1627 | 78.7932 | 89.3163 | 90.6594
PM2.5 (g/kgF) | 6.9 | 8.2233 | 4.3095 | 10.2633 | 0.59284 | 1.3838
Ecodesign η (%) | 30 | 65 | 65 | 65 | 79 | 79
Ecodesign (g/kg) | 6 | 5 | 5 | 5 | 2.5 | 2.5
Heat output (kWth) | 2.1457 | 2.1457 | 7.881 | 7.881 | 6.3489 | 6.3489 | 5.0405 | 5.0405 | 4.6623 | 4.6623 | 7.1338 | 7.1338
More inorganic matter…

## Slide 12: Advanced interventions Field investigations
CPC/temp-RH (UFP)
variations outdoors
CPC/temp-RH (UFP)
variations indoors
PM2.5
temp/RH
Particles
size ranges
CO, TVOCs
variations
Low energy house in Oslo, Norway
Foto by Barbosa, 2014
R. L. Carvalho et al, “Wood-burning stoves in low-carbon dwellings,” Energy Build., vol. 59, pp. 244–251, 2013.

## Slide 13
Hwam auto-pilot, Denmark
Aduro smart response, Denmark
Digital
Manual
Advanced interventions
Emerging devices

## Slide 14: Advanced interventions Overheating & energy savings
Chart: Net thermal energy production (MWh)
| Espergaede (1977) | Værløse II (1985) | Bagsværd (1998) | Hillerød (2001) | Ringsted (2006) | Virum (2007) | Værloese (2008) | Esrum I (2009) | Esrum (2009) | Lasby (2008) | Skandenborg (2011) | Langhus (2011)
Wood burning | 8.1054 | 6.6788 | 5.0091 | 5.27 | 3.353 | 0.98225 | 1.054 | 2.635 | 4.216 | 8.3689 | 3.9852 | 3.1488
Other heating systems | 31.581 | 8.712 | 14.157 | 9.801 | 7.81 | 15.246 | 11.979 | 8.5 | 12 | 6 | 3.269 | 16.316
Smart control
ca. intake out
Manual
>50% supply
Primary heat!
Overheat
Overheat
Area~120-400 m2
New
Old
Smart control

## Slide 15
digital
manual
IAQ
#/cm3
Time (hours)
New envelope &
Indoor intake
New houses &
Outdoor intakes
Advanced interventions
”Draft design” & variations on IAQ
Old chimney &
Indoor intake
Lightning
Refilling
Background

## Slide 16: Outcomes & further work Household wood-heating interplays
Low losses/wattage
Mid losses/wattage
High losses
ADVANCED
”ash & oxidative”
IMPROVED
”burning with flames”
TRADITIONAL
”smouldering”
Eg. Europe
Eg. Southern EU
Eg. Scandinavia
New testing approaches of the actual interplays are recommended to support innovation and air quality management processes…

## Slide 17
Thanks for listening!
https://woodburningstovesblog.wordpress.com/