## Slide 1: Calculating Energy Efficiency Using A Chemical Mass Balance Method
Crispin Pemberton-Pigott
Reporting research on the combustion of solid fuels conducted at
SeTAR Centre, University of Johannesburg
Cape Peninsula University of Technology, Cape Town
China Agricultural University, Beijing
Presented at
Brookhaven National Laboratory – 7 April 2016

## Slide 2: Problem Statement
=Test methods assume that the fuel burns and dries
homogeneously
If this was true there would not be a
“char-burning phase”
Emissions and efficiency are miscalculated because of this assumption

## Slide 3: Energy Efficiency:
An efficiency is a ratio:
Useful Energy Delivered . X 100%
Energy available in the fuel consumed
Consumed: Combusted to the point where remainder is abandoned

## Slide 4: Energy Efficiency:
An efficiency is a ratio:
Useful Energy Delivered . X 100%
Energy available in the fuel consumed How is this determined?
Consumed: Combusted to the point where remainder is abandoned

## Slide 5: Fuel Analysis – MASHCON
M Moisture
A Ash
S Sulphur
H Hydrogen
C Carbon
O Oxygen
N Nitrogen
HHV Higher Heating Value

## Slide 6: Fuel Analysis – MASHCON – Examples
Ultimate analysis (dry) in a mass basis

## Slide 7: Fuel Analysis – MASHCON – Multi-fuel
Determination of the fuel composition can be challenging

## Slide 8: Fuel Analysis – MASHCON
Determination of the fuel composition can get complicated II
As Burned Ash-Free heat content - ABAF

## Slide 9: Collect the Products of Combustion
Tracking the combustion is challenging too B.E.S.T. Lab, CAU College of Engineering

## Slide 10: Heat Gained – Space Heating
Calculate what energy was available in the fuel
Calculate the losses up the stack
Siegert Method – estimates losses up the stack
Gas-by-gas calculation – estimate losses up the stack
Heat Gained, by subtraction

## Slide 11: Step 1: Combust the Fuel
Remove the ash and convert to Molar Elements

## Slide 12: Step 1: Combust the Fuel
Combust in Air
Water Vapour 74,000 ppm

## Slide 13: Assumptions
1. Hydrogen and Oxygen are present in the Fuel and Water in known ratios
Fuel O and Fuel H are released homogeneously from biomass even if the
fuel burns inhomogeneously

## Slide 14: Assumptions
1. Hydrogen and Oxygen are present in the Fuel and Water in known ratios
Fuel O and Fuel H are released homogeneously from biomass even if the
fuel burns inhomogeneously
All three are simultaneously true

## Slide 15: De-combustion

## Slide 16: De-combustion
Check for a fuel moisture deficit or surplus
The HHV of this “fuel” is used in the denominator of the Efficiency calculation

## Slide 17: Significance of Real-Time Fuel Analysis
The HHV can be calculated in real time as the fuel evolves
The CO2MAX value can be calculated in real time

## Slide 18: Significance of Real-Time Fuel Analysis
The HHV can be calculated in real time as the fuel evolves
The CO2MAX value can be calculated in real time
The ratio of the oxygen provided by air to the total oxygen demand can be determined in real time [StOxR]

## Slide 19: Significance of Real-Time Fuel Analysis
The HHV can be calculated in real time as the fuel evolves
The CO2MAX value can be calculated in real time
The ratio of the oxygen provided by air to the total oxygen demand can be determined in real time [StOxR]
The stoichiometric volume of combustion gases can be calculated using StOxR.
From this the diluted volume of gases can be calculated using the Excess Air level.
The concentration of pollutants in that volume can be determined.

## Slide 20: Significance of Real-Time Fuel Analysis
The HHV can be calculated in real time as the fuel evolves
The CO2MAX value can be calculated in real time
The ratio of the oxygen provided by air to the total oxygen demand can be determined in real time [StOxR]
The stoichiometric volume of combustion gases can be calculated using StOxR.
From this the diluted volume of gases can be calculated using the Excess Air level.
The concentration of pollutants in that volume can be determined.
The mass of emissions can be reported more accurately per measurement interval.

## Slide 21: Why is this an improvement?
Two different approaches can be made:
1. Assume the fuel burns and dries homogeneously
Assume this is not the case but that the Oxygen and Hydrogen are released
from the fuel homogeneously
The Chemical Mass Balance assumptions provide an analysis that more closely represents what is actually happening in a solid fuel fire.

## Slide 22: Why is this an improvement?
Two different approaches can be made:
1. Assume the fuel burns and dries homogeneously
Assume this is not the case but that the Oxygen and Hydrogen are released
from the fuel homogeneously
The Chemical Mass Balance assumptions provide an analysis that more closely represents what is actually happening in a solid fuel fire.
Fuel O to Fuel H
Water O to Water H
Measured ∑O to Measured ∑H

## Slide 23: Thank you!
Appreciations:
Staff and graduate students at:
The SeTAR Centre, Research Village, University of Johannesburg, Department of Geography, Environmental Management and Energy Studies, JHB, R.S.A.
Chinese University of Agriculture, College of Engineering, Beijing, China
Cape Peninsula University of Technology, Cape Town, R.S.A.
This work represents personal efforts and was not funded.

## Slide 24
Bishkek, Kyrgyzstan 2016 Haidian North, China 2016