## Slide 1: The “Lumburnator” a Next Generation Wood Stove
Student Team:
Jake Lindberg, JinYing Lin,
Kevin J. Lee, Yunxiao Jiang, Jason Peng
Advisors:
Dr. Devinder Mahajan, Dr. Jon Longtin, *Dr. Vladimir Zaitsev,
Dr. Tom Butcher (BNL)

## Slide 2: Introduction
*According to the EIA Winter Fuels Report:
• Wood as primary heat up by 33%
• 2.6 million home’s primary heat
• 9.8 million home’s secondary heat
**EPA expects 113,000 wood stoves to be sold in 2015
**Mandates by 2020:
• 2.5 g/hr PM2.5
• 70% reduction in VOCs
• 62% reduction in CO
*"Short Term Energy Outlook (STEO)." Energy Information Administration - EIA - Official Energy Statistics from the U.S. Government. N.p., 8 Mar. 2016. Web. 6 Apr. 2016.
**Standards of Performance for New Residential Wood Heaters, New Residential Hydronic Heaters and Forced-Air Furnaces. Rep. 50th ed. Vol. 80. N.p.: EPA - Environmental Protection Agency, n.d. 16 Mar. 2016. Web. 6 Apr. 2016.

## Slide 3: Scope of Work
• Subtask 1.1 Design and Fabricate Firebox
• Subtask 1.2 Propane burner system
• Subtask 1.3 Airflow Design
• Subtask 1.4 Completion of the Year One Lumburnator
• Subtask 1.5 Participate in 2016 Design Challenge
**Subtask 2.4 Onsite Testing

## Slide 4: The Firebox
Firebox Dividers:
• Separate fuel charges ➡ reduction in Burn Rate (BR)
• Increase residence time and turbulence
Dual chamber system:
• Thermally oxidizes emissions
• Enables staged combustion

## Slide 5: Intermediate Results...

## Slide 6: Afterburner
• Propane fired afterburner thermally oxidizes VOC and CO
• Effective during pre-burn
• Propane can be used for push-button ignition

## Slide 7: The Airflow System
• Draft Control ➡ BR control
• Enables electronic process control
• Induction results in dilution and cooling of flue gas
- Dilution important for
measurement systems
- Cool gas needs means
smaller chimney
Venturi Draft Inducer

## Slide 8: Setup
• Scale ⇾ burn rate evaluation
• Anemometer ⇾ draft/dilution ratio measurements (CV)
• Draft Gauge ⇾ draft changes (PCV)
• Thermocouples – location specific temperatures (PCV)
PCV = process control variable
CV = control variable

## Slide 9: Future Work
Subtask 2.1 Catalytic Combustion
Subtusk 2.2 Control system
Subtask 2.3 Ignition System
**Subtask 2.4 Onsite Testing
Subtask 2.5 Participate in 2017 Woodstove Design Challenge

## Slide 10: Thanks!
With special thanks to NYSERDA and Robert Carver, Brookhaven National Laboratory and Dr. Tom Butcher, Stony Brook University and professors Devinder Mahajan, Sotirios Mamalis, Benjamin Lawler, and Jon Longtin.

## Slide 11: Questions?
Student Team Photo